## Slide 1
Landscaping and Home Design for Wildfire Defense
Presented by UCCE Master Gardeners of [NAME]County
August 24, 2015
Content Credit: Yana Valachovic, UCCE Forest Advisor & County Director - Humboldt and Del Norte
Robin Stanley, UCCE Master Gardener of El Dorado County
Steve Quarles, UCCE Advisor Emeritus
Notes: ** Before giving presentation – please watch the original presentation from Yana Valachovic for information and details that pertain to these slides, LINK: https://uc-d.adobeconnect.com/_a841422360/p72wo3t2hjc/?launcher=false&fcsContent=true&pbMode=normal **. Questions? Contact the UC Master Gardener Program statewide office, mg.ucanr.edu

## Slide 2
Table of Contents:
  Wildfire context
  How homes burn from wildfire
  Defensible space
  Interaction between the vegetation, landscaping and home condition
  Resources

## Slide 3
Wildfire is important!
Some plant species need fire to germinate, establish or reproduce
Keeps forests and rangelands open
Maintains oak woodlands
Can promote wildlife habitat
Removes fuels to reduce the occurrence of high intensity wildfire
Photo credit: Michael Poe, UC ANR
Notes: NOTES: Yosemite National Park wildfire damage

## Slide 4
Fuels are growing faster than we are treating them …
Graphic courtesy of Malcom North (USDA Forest Service)

## Slide 5
Stages of wildfire
Photo credit: Landscape and Building Design for Bushfire Areas. Ramsay & Rudolph, CSIRO
Notes: A building will be exposed to the main flame front of a wildfire for a relatively short period of time – 5 to 10 minutes at the most.
2. / 3. A building will be exposed to pre- and post-fire for a much longer time.

## Slide 6
How does a house burn from wildfire?
Ember / Firebrand
Photo credit: Insurance Institute for Business and Home Safety
Notes: A house can burn from any of these types of exposures:
ember/firebrand
Radiant heat
Flame contact

## Slide 7
How does a house burn from wildfire?
Ember / Firebrand
Radiant Heat
Photo credit: Tennessee Division of Forestry
Notes: A house can burn from any of these types of exposures:
ember/firebrand
Radiant heat
Flame contact

## Slide 8
How does a house burn from wildfire?
Flame Contact
Flame Contact
Photo credit: Insurance Institute for Business and Home Safety
Notes: A house can burn from any of these types of exposures:
ember/firebrand
Radiant heat
Flame contact

## Slide 9
Know the basics of fire:
Fuel + Oxygen + Heat = Fire
  Which of these three can you control?
Fuel is… anything that will burn
  Dry or dead vegetation
  Wood siding, roofing, fencing
  Trees
  Woody shrubs or perennials
  Landscape mulch
Photo credit: MorgueFile.com – 46birds

## Slide 10
The fuel challenge …
Long-distant embers can ignite fuel on your house
Ground fire can approach your house
We’ll focus on landscape fuel issues first, and house vulnerabilities second.

## Slide 11
California Law (2008)
  State law extended the defensible space around your home from 30 to 100 feet. This doesn’t sound like much, just 70’, but compare the area:
  area with 30’ clearance = 2,826 ft2
  vs.
  area with 100’ clearance = 31,400 ft2
11X MORE AREA!

## Slide 12
Flame Contact
Photo Credit: CAL FIRE
Notes: Defensible space zone (30 feet)

## Slide 13
Understand the zones …

## Slide 14
What does the law say?
Zone spacing depends on the slope, height of vegetation and fire risk:
  Steeper slope = more spacing
  Taller vegetation = more spacing
  More fire prone = more spacing
Identify your two zones:
  0 - 30 feet - Defensible Space Zone
  30 - 100 feet - Reduced Fuel Zone

## Slide 15
Spacing
6 ft to 20 ft. depending on slope and vegetation size/type (2x)
x
2 X
10 ft. to 30 ft.
depending on slope and vegetation type and size
x
4 x
20-40% slope
30 ft. or more
depending on slope and vegetation type and size
x
6 x
Over 40%

## Slide 16
Eliminate fuel ladders

## Slide 17
Photo credit: UCCE Master Gardeners of El Dorado County

## Slide 18
Photo credit: Insurance Institute for Business and Home Safety

## Slide 19
Photo credit: UCCE Master Gardeners of El Dorado County

## Slide 20
Photo credit: UCCE Master Gardeners of El Dorado County

## Slide 21
Home defense zone

## Slide 22
Photo credit: UCCE Master Gardeners of El Dorado County
Thin and separate
Create islands
Cut grass
Favor trees away from the house

## Slide 23
DON’T overplant!
Photo credit: Rancho Santa Fe Fire Protection District

## Slide 24
Incorporate a fuel mosaic
Photo credit: UCCE Master Gardeners of El Dorado County

## Slide 25
Incorporate nature and hardscape
Photo credit: UCCE Master Gardeners of El Dorado County

## Slide 26
Consider hardscape
Photo credit: UCCE Master Gardeners of El Dorado County

## Slide 27
Separate vegetation from the house

## Slide 28
0 - 5 feet “noncombustible zone” to reduce chance of flame contact exposure
Photo credit: Insurance Institute for Business and Home Safety
Notes: BACK of home – appropriate defensible space around house

## Slide 29
Effective defensible space must be present on all sides of the home
Photo credit: Insurance Institute for Business and Home Safety
Notes: FRONT of home – does not have accurate defensible space

## Slide 30
Near the house, keep it green and healthy
… but don’t forget to conserve water!
Photo credit: UCCE Master Gardeners of El Dorado County

## Slide 31
Fire resistant plant lists?
All plants can burn regardless of how they are marketed
Fire safe landscaping requires maintenance (pruning, irrigation, clean-up)
Select low growing, open structured, less resinous, higher moisture content plants
Native and drought tolerant plants can be options, if maintained well

## Slide 32
Mulch helps plants retain moisture, but it will burn too!
Use hardscape, rock mulch or lawns < 5 feet from the home.
Rubber mulch
Photo credit: University of California Cooperative Extension
Pine needle mulch
Bark mulch

## Slide 33
Under vents and eaves
Adjacent to siding
Under or near decks
Inside corners
Where to not plant

## Slide 34
Simulated embers exposure on a house

## Slide 35
Vulnerable to ember entry
More so than vent in a soffited eave
Open eave vents:

## Slide 36
Litter accumulation creates exposure to the wall unit (not protected with roofing).

## Slide 37
Embers can ignite litter in rain gutters
Photo credit: Insurance Institute for Business and Home Safety

## Slide 38
Plastic gutters
vs.
Metal gutters
Photo credit: Insurance Institute for Business and Home Safety

## Slide 39
Firewood stored too close to the house, led to fire inside the garage.
Photo credit: Insurance Institute for Business and Home Safety
INSIDE
Hardboard Siding

## Slide 40
Stored building materials under a deck is vulnerable
INSIDE
Photo credit: University of California Cooperative Extension
Photo credit: Insurance Institute for Business and Home Safety

## Slide 41
Firewood under a deck

## Slide 42
Broom

## Slide 44
INSIDE
Photo credit: Insurance Institute for Business and Home Safety
A neighbor’s house could be in the 5 -30 foot zone- their condition can affect your survival.

## Slide 45
INSIDE
For more information visit:
ucanr.edu/sites/forestry/Wildfire

## Slide 46
Conclusions
Landscape
Fire safe landscapes can be beautiful, safe, maintain privacy and save water
Placement of vegetation is key (away from vents, eves and decks)
Maintenance is essential
  0 – 5 feet (non-combustible materials only)
  5 – 30 feet (lean, green and clean)
  30 – 100 feet (reduced fuel zone)

## Slide 47
Conclusions
House
Remove stored fuels and debris, clean gutters, maintain or improve roofing (class A)
Choose fire resistant building products during your next house project

## Slide 48
Photo credit: Home Survival in Wildfire Prone Areas

## Slide 49
UCCE Master Gardeners are here to help! Contact us:
Website: [Insert] Phone: [Insert]
Email: [Insert]

## Slide 50: Thank you! Questions?