## Slide 1
Ventura county
Stormwater runoff management from plastic tunnels.
Oleg Daugovish, Ben Faber, Eta Takele, Anna Howell, Camille Garcia and Gina Ferrari (UC-ANR), Jamie Whiteford (and Ventura County Resource Conservation District staff), Laosheng Wu (UC-Riverside, and his lab staff).

## Slide 2: SB County: Hoop Structures Ordinance Amendment ( Project) Environmental Impact Report (EIR)
“If multiple hoop structures are arranged together in rows, the covers will direct runoff to the narrow portions of ground surface located in between the individual rows (i.e., “anchor row” or “post row” gutters). Over time, the concentration of runoff into these newly channelized gutters can create a scouring effect that would result in increased soil erosion, exacerbated by increased runoff velocities within the gutters. Increased soil erosion can lead to greater silt and sediment levels in the runoff, which could adversely affect surface water quality.”

## Slide 3: SB County: Hoop Structures Ordinance Amendment ( Project) Environmental Impact Report (EIR)
“..agricultural operators are subject to the Ag Order 3.0, which includes a number of requirements to reduce storm water runoff and velocity and hold fine particles in place”

## Slide 5
Untreated post row

## Slide 6
Chart: Sowthistle weed number/100ft of post row on Feb 12, 2013
| barley | barley partial | triticale | triticale partial | bare control
Column1 | 0.6 | 2 | 0.6 | 3.3 | 58.6
Untreated (bare control) > rest (at P=0.05)

## Slide 7
Chart: Horseweed (Conyza app.) weed number/100ft of post row on Feb 12, 2013
| barley | barley partial | triticale | triticale partial | bare control
Column1 | 0.3 | 0.3 | 7.3 | 18 | 126
Untreated (bare control) > rest (at P=0.05)

## Slide 8
Chart: Seedbank weeds (little mallow, filaree, shepardspurse) number/100ft of post row on Feb 12, 2013
| barley | barley partial | triticale | triticale partial | bare control
Column1 | 3.3 | 5.3 | 6.3 | 53.3 | 47

## Slide 9: 2016-2018 SCBG project: Ventura and SB counties

## Slide 10
Untreated (standard)
Barley cover crop
planted at 500lbs/A,
terminated at heading
with sethoxydim and
mowing, as needed
Yardwaste mulch
(1-4 inch particles)
applied 2-3 inches thick

## Slide 11
Polyacrylamide
(PAM, ‘Simplot
Soilbuilder’ )
applied at ~2lbs/A
before rain events
Weed barrier
fabric placed on
soil surface and
pinned

## Slide 12: Polyacrylamide (PAM)
Synthetic Organic Polymer, breaks down to monomers by physical degradation, used >1mln acres in US
PAM itself does not pose any environmental threat, as long as acrylamide (breakdown monomer) is kept away from food. Use anionic PAM, with <0.05% acrylamide
Require clay particles in soil (not pure sand)
Stabilizes soil aggregates
Image by Mike Cahn

## Slide 13: Rainwater
Surface runoff
Infiltrates towards groundwater

## Slide 15: Turbidity of runoff
PAM
Barley
Untreated
Mulch
Weed barrier

## Slide 16: Turbidity in 2017 (grab samples, Somis)
Chart: Nephelometric turbidity units
| barley | fabric | mulch | PAM | untreated
1/20/2017 | 215 | 96.3333 | 21 | 358.6667
2/10/2017 | 168 | 162.3333 | 92.5 | 44.6333 | 358.6667
2/17/2017 | 178 | 84.3333 | 9.5 | 231 | 379.6667
3/21/2017 | 254.6667 | 90.6667 | 155 | 485.6667 | 614.6667
Untreated > rest (at P=0.05) at all dates, except PAM 3/21/17

## Slide 17: Turbidity in 2018 (grab samples, Somis)
Chart: Nephelometric turbidity units
| barley | fabric | mulch | PAM | untreated
1/8/2018 | 143 | 34 | 42 | 105 | 414
3/1/2018 | 87 | 128 | 42 | 75 | 696
3/10/2018 | 138 | 245 | 291 | 109 | 800
Untreated > rest (at P=0.05)
Turbid runoff
from gopher hole

## Slide 18: Turbidity in 2018 (first flush): Somis
Untreated > rest (at P=0.05)
Chart: 
| Barley | Fabric | Mulch | PAM | Untreated
1/8/2018 | 81 | 147 | 776 | 501
2/14/2018 | 58 | 302 | 73 | 351 | 883
3/1/2018 | 697 | 288 | 118 | 344 | 1985
3/10/2018 | 337 | 110 | 92 | 274 | 3475
3/13/2018 | 195 | 173 | 165 | 104 | 2545
3/16/2018 | 636 | 513 | 232 | 155 | 2072
3/21/2018 | 275 | 93 | 130 | 53 | 1717
No PAM applied
Soil from plastic removal
After replanting

## Slide 19: Turbidity at 5 dates in 2018 (first flush): S. Maria
Untreated > rest (at P=0.05) at most dates
Chart: NTU
| Barley | Fabric | Mulch | PAM | Untreated
3/10/2018 | 337 | 110 | 92 | 274 | 3475
3/14/2018 | 473 | 306 | 238 | 355 | 3772
3/16/2018 | 228 | 315 | 33 | 407 | 3170
3/20/2018 | 406 | 69 | 79 | 68 | 1049
4/7/2018 | 217 | 91 | 95 | 100 | 368

## Slide 20: Sediment in 2018 (after 3.25”rain)
Chart: g,dry/5 gal bucket
| Barley | Fabric | Mulch | PAM | Untreated
Somis | 40 | 2908 | 0 | 78 | 5552
Santa Maria | 530 | 1598 | 465 | 1262 | 6828
Untreated > rest (at P=0.05)
Soil moved from bed sides on fabric

## Slide 21: Sediment in 2018 (after 0.1”rain, S. Maria)
Chart: g,dry/5 gal bucket
| Barley | Fabric | Mulch | PAM | Untreated
 | 17 | 41 | 12 | 148 | 605
Untreated > rest (at P=0.05)

## Slide 22: Mangiafico et al. 2009- Hort Technology (work from Ventura county)
Constituents in runoff exceeding benchmarks for surface waters included turbidity, chlorpyrifos, and some organochlorine pesticides. When detected, chlorpyrifos concentration was linearly related to sample turbidity (P = 0.0025, r2 = 0.49). This suggests that the retention of waterborne sediments on-site may be an effective method for mitigating runoff of this pesticide.

## Slide 23: Phosphorus in first flush of runoff, Somis
Chart: mg/L
| 43108 | 43145 | 43158 | 43169 | 43172
Barley | 0 | 3.984 | 0 | 2.5967 | 2.0287
Fabric | 4.6533 | 4.3093 | 3.1773 | 2.1467 | 1.6827
Mulch | 3.4873 | 2.783 | 1.529 | 1.011 | 1.116
PAM | 3.0607 | 3.178 | 4.447 | 2.1433 | 1.2807
Untreated | 6.1773 | 5.6353 | 5.061 | 3.324 | 7.3553
24-85% less than from untreated soil

## Slide 24
NO3-N in runoff (first flush), averaged of 5 sampling events
Significantly < than untreated (P=0.05) during 1 (barley) or 2 (mulch) out of 5 rain events,
BUT
Reduced flow in mulch and barley during light rain = lower or no runoff compared to other
Chart: Santa Barbara County Runoff
| Barley | Mulch | PAM | Fabric | Untreated
 | 1.1215 | 1.4146 | 2.7828 | 2.3181 | 1.4368
Chart: Ventura County Runoff
| Barley | Mulch | PAM | Fabric | Untreated
 | 1.8064 | 0.52084 | 3.1998 | 3.1998 | 2.3154

## Slide 25
Chart: 8" lysimeters Santa Barbara County
| Barley | Mulch | PAM | Fabric | Untreated
8" deep | 5.3492 | 7.4182 | 10.3692 | 17.5308 | 13.9564
Chart: 8" & 24" lysimeters Ventura County
| Barley | Mulch | PAM | Fabric | Untreated
8" deep | 1.8544 | 9.7213 | 14.4875 | 10.6957 | 15.7543
24" deep | 3.4463 | 2.678 | 28.1 | 13.52 | 8.3517
NO3-N in leachate, averaged of 5 sampling events
Significantly (P<0.05) < than untreated

## Slide 26: Soil analyses under treatments, Somis, Apr 2018
 | Moisture, % | At P=0.05 | NO3-N, ppm | At P=0.05
Untreated | 18.5 | b | 28 | a
Fabric | 18.4 | b | 22 | a
Mulch | 20.8 | a | 7.8 | b
Barley | 19.6 | ab | 4.4 | b
PAM | 18.3 | b | 35 | a
No differences in phosphorus among treatments or
among soil depths (0-6” and 6-12”)

## Slide 27: Soil analyses under treatments, S. Maria, Apr 2018
 | NO3-N, ppm | At P=0.05
Untreated | 11.2 | a
Fabric | 2.3 | b
Mulch | 9.8 | ab
Barley | 4.7 | b
PAM | 8.4 | b
No differences in moisture or phosphorus levels
among treatments or soil depths (0-6” and 6-12”)

## Slide 28
Chart: Raspberry shoots in post rows, Somis
| Fabric | Mulch | Barley | PAM | Untrearted
 | 29 | 371 | 112 | 141 | 77
Mulch > other (P=0.001)

## Slide 29
Chart: Weeds in post rows, Somis
| Weed barrier | Barley | Mulch 2.5" | PAM | Untreated
11/23/2016 | 4.3333 | 27 | 21 | 173.6667 | 206
2/15/2017 | 10 | 338 | 128.6667 | 484.6667 | 651
1/17/2018 | 0 | 1686 | 90 | 610 | 625
Germinated after re-seeding,
controlled by mowing

## Slide 30
Chart: Weeds in post rows, S. Maria
| Weed barrier | Barley | Mulch 2.5" | PAM | Untreated
2/1/2017 | 0 | 0.33 | 4.7 | 2.3 | 7
4/6/2017 | 0.7 | 42 | 65 | 52 | 76
2/16/2018 | 11 | 138 | 99 | 136 | 244

## Slide 31: Key points
All treatments can have beneficial impact on soil and nutrient retention and weed control (except PAM) if maintained/properly managed:
Barley: dense stands control weeds, but poor stands and scarce residue do not. If stand is poor and residue after mowing/herbicide use is lacking- consider reseeding. 600 lbs/a rototilled in moist soil or before rain works best.
PAM: spread before rain and minimize soil disturbance. If not disturbed can benefit during multiple rain events. If disturbed – re-apply. Will not affect weeds.
Mulch: Controls annual weeds only when persists at ~2.5-3 in thickness. Can float out of the ends of tunnel at high runoff velocity. If thin layer/breaks down rapidly - minimizes efficacy
Fabric: Best weed control; minimize soil on top of fabric . It can be rolled up at the end and reused.

## Slide 32: Key points
Barley and mulch retain moisture and reduce N moving to groundwater better than other treatments or untreated.
This N is likely used by barley crop, and for residue and mulch decomposition (cellulose and lignin degrading m/o)
Mulch promotes caneberry shoot growth in it, likely by retaining moisture.
All BMPs reduced development of erosion channels compared to untreated.
For workers in tunnels: no issues with any BMPs , barley in the center or/and cut to <6” from ground.

## Slide 33: Sample costs of post row treatments
Treatment | Cost/Tunnel cycle (3 yrs) Per Acre (5.5 post rows)
Fabric (weed barrier) | $ 163
Mulch | $ 193
Cover crop (barley 500lbs/A) | $ 59
PAM | $ 192
Benefits?
Reduce Costs of sediment management 60-90%
Reduce or eliminate penalties for non-compliance if runoff is polluted (phosphorus, sediment, chlorpyrifos /other soil-adsorbed pesticides)
Keeping soil in your field and reducing erosion, especially on slopes
Barley and mulch reduced nitrate leaching to groundwater
Opportunity to market your product as from ‘farm that practices soil conservation’ , CDFA ‘Healthy Soils’ Program has funding for growers

## Slide 34
ACKNOWLEDGEMENTS
We greatly acknowledge help and contributions from Driscoll/Reiter AC, AGQ lab and funding from Cal Dept of Food and Agriculture.